## Slide 1: CS321: Friday Tutorial
Tushar Semwal

## Slide 2: MQ Telemetry Transport (MQTT)

## Slide 3: MQTT: Basics
A lightweight messaging protocol
Publish/Subscribe
For M2M telemetry with low-bandwidth and -footprint
Created by IBM in 1999 for Oil pipeline telemetry via satellite. NOW OPEN SOURCE

## Slide 4: By the way
Telemetering means??
Tele + Metering
Tele = Far or Remote
Metering = Measurement
Remote Measurements and sending data to the base server

## Slide 5: Terms
Client: A “device” that publishes a message or subscribes to a topic
Publish: A client sends a message
Subscribe: The broker sends the message about the topic to which a client is subscribed to.
Topic: A namespace (casually, address string) to/from which clients publish and subscribe
Broker: A “server” which accepts messages and delivers messages from/to clients

## Slide 6: Model
Broker
Subscriber-1
Subscriber-2
Subscriber-3
Publisher-1
Publisher-2
/topic-A
/topic-B
/topic-A
/topic-B
/topic-B

## Slide 7: Why not HTTP?
Lot of header. Too big. MQTT smallest packet size is just 2 bytes
Request/Response
Usually synchronous. MQTT is asynchronous.

## Slide 8: Usage
Facebook Messenger (mobile app) uses MQTT to minimize latency and battery usage (https://ibm.co/2vNa8Uk)
St Jude Medical, who use MQTT to remotely monitor patient implants (https://ibm.co/2JfCNWK)
Consert, use MQTT as a part of their real-time home energy monitoring and management solution

## Slide 9: Broker
Open source implementations are available:
Mosquitto (https://mosquitto.org/)
Mirco Broker (https://github.com/micro/go-micro)

## Slide 10: CS321: Use Case
Temperature sensor
Accelero
/group1/temp1
/group7/acc1
Group 3
CSE Office

## Slide 11: Resouces
https://www.baldengineer.com/mqtt-tutorial.html
https://github.com/256dpi/arduino-mqtt

## Slide 12: Embedded Programming
What is so different?

## Slide 13: Difference
PC/Mobile
General purpose
Over 1MB of memory
High performance CPU
No energy constraints
Goal: overall performance
Embedded System
Specific digital control
Memory in Kbs
Low-end MCU
Energy constraint
Goal: Attain required performance at the lowest cost

## Slide 14: Why Memory is limited?
Few variables are enough for digital control
Less area
Low cost
Less energy
Address <= 16 bit
CPU
Cache
Main Memory
Disk
CPU
RAM
ROM
MPU chip
Mother Board
Embedded System

## Slide 15: Power Consumption
int main(void)
{
Initialize();
while(1)
{
do_some_useful_work();
hibernate(2ms);
}
}

## Slide 16: Choosing the Right Data Type
Memory: Smaller variables
Storage: Smaller constants and program

## Slide 17
<stdint.h>
uint8_t
uint16_t
uint32_t
int8_t
int16_t
int32_t

## Slide 18: Floating point
Be very careful
Usually NO FPU
Software managed
Avoid usage if possible

## Slide 19: Check memory usage with Arduino
handson

## Slide 20: Takeaways
Use portable fixed size types
Use smallest type possible
Use floats only if necessary

## Slide 21: Defining Qualifiers is IMPORTANT!!
Qualifiers determine where the variable is stored and other stuffs:
  Memory: Stored in RAM
  Storage: Stored in ROM
  Hardware: letting hardware directly access some variables for e.g. registers
  Compiler optimization control

## Slide 22: Quiz
int a;
int b;
void experiment(){
a=8; b=a*7;
If(a==8)
printf(“a equals 8”)
else
printf(“a NOT equals 8”)}
What is the ouput?
  a equals 8
  a NOT equals 8
  Can’t say – I am a loser =D
Is it possible to execute the ELSE part?
  YES
  NO

## Slide 23: Quiz – why?
int a;
int b;
void experiment(){
a=8; b=a*7;
If(a==8)
printf(“a equals 8”)
else
printf(“a NOT equals 8”)}
Multiprocessors with shared memory
Multithreading
Hardware attached variables Or memory mapped I/O
Interrupts

## Slide 24: Volatile Qualifier – Quick fix
volatile int a;
int b;
void experiment(){
a=8; b=a*7;
If(a==8)
printf(“a equals 8”)
else
printf(“a NOT equals 8”)}

## Slide 25: Takeaways
The volatile qualifier informs the compiler that variable may change because of hardware or other means
Use to explicitly avoid optimization

## Slide 26: Constants – const qualifier
const int ledPin = 13;
#define ledPin 13
const stored in ROM
#define also stored in ROM but copied wherever used in program
#define simply replaces text
  GOOD: easy to change the value of a constant
  BAD: code bloating and no type or syntax checking – runtime errors!!
const send to ROM once – memory addressing
  GOOD: Large constants will be stored once, better for double, long
  BAD: practically NONE

## Slide 27: Function Alternatives
Memory: Traditional functions are put in stack
Storage: Look Up Tables (LUT) and Inline functions are stored in ROM
Processing power: LUT are easy on CPU

## Slide 28: Look Up Tables
Constant Arrays containing a collection of return values
e.g. const float log_LUT[256] = {-1.0E-30, 0.0000, 0.693147, ….}
Multiplication tables we learned
Some scientific calculators have LUTs
uint8_t x;
float y;
y = log(x);
y = log_LUT[x]
e.g. IMU Euler angle calculations

## Slide 29: Macro Functions
#define square_macro(x) x*x
Advantages
  No need to send or return values – a bit fast
  Readability
Disadvantages
  Code bloating

## Slide 30: Inline Functions
While regular functions may take time to execute AND Macros can be troublesome
Inline provides best of both
Identical to regular functions
Just write inline while writing function definition
Advantages over Macro
  Parameters are inspected
  Debugging is easier

## Slide 31: Forced vs Suggested Inlining
int square_AI(unsigned char x)__attribute__((always_inline));
//Always Inline
int square_AI(unsigned char x){
return x*x;}
//suggested Inline
int inline square_SI(unsigned char x){
return x*x;}

## Slide 32: Takeaways
Macros are okay for simple functions
If you need inlining, you may force it on compiler
Otherwise leave inlining to compiler

## Slide 33: Thank You!
Questions?